| Customer: | Rohde & Schwarz – Philippines | Tested By: | S. PALACIO |
| --- | --- | --- | --- |
| SO No: | SO14-334-F-P | Temperature: | +25°C |
| Model No: | HP20G-19D5G-CD-292FF | Date: | 11/13/2014 |
| Serial No: | PL16137/1444 | Drawing No: | 27610684 | Rev: | A1 |

| Test. Item No | PARAMETERS | SPECIFIED VALUE | TEST RESULTS | qa qc |
| --- | --- | --- | --- | --- |
| 1 | Pass-band: | 20 to 40 GHz | 20 to 40 GHz See Plot |  |
| 2 | Passband Insertion Loss: | 1.5 dB Max. | 0.68dB See Plot |  |
| 3 | Rejection | 54 dB @ 14.5 GHz | 54.08dB See Plot |  |
| 4 | Pass band VSWR | 2.0:1 Max | 1.97:1 See Plot |  |

| QA/QC Approval: |  | Date: |  |
| --- | --- | --- | --- |