| Customer: | RFSS (CA) | Tested By: | S.Baughman |
| --- | --- | --- | --- |
| SO No: | SO15-062-P-P | Temperature: | +25°C |
| Model No: | TD-30T-SHS-218-2G4G-PECL | Date: | 03/23/2015 |
| Serial No: | PL16888/1513 | Drawing No: | 27621473 | Rev: | A1 |

| Test. Item No | PARAMETERS | SPECIFIED VALUE | TEST RESULTS | qa qc |
| --- | --- | --- | --- | --- |
| 1 | Frequency Range: | 2 TO 18 GHz (Optimized 2-4 GHz) | 2 TO 18 GHz (Optimized 2-4 GHz) |  |
| 2 | VSWR: | 3.0: 1 Max @ -20dBm | 2.66:1 See Plot |  |
| 3 | Minimum Signal Level for Logic 1: | -20 dBm @ 2.0 GHz | -20.5 dBm @ 2.0 GHz |  |
| 4 | Threshold Variation over Frequency (Any 1 GHz Window) | ± 0.5 dB | ± 0.32 dB |  |
| 5 | Minimum Signal Level for Logic 0 | -25 dBm | -22 dBm |  |
| 6 | Dynamic Range: | +10 dBm Max | +10 dBm |  |
| 7 | Propagation Delay from 50% of an input of -20 dBm | 15 ns Max | See Typical Characteristics |  |
| 8 | Propagation Delay from 50% of an input of +10 dBm | 15 ns Max | See Typical Characteristics |  |
| 9 | Output Logic: | LVPECL Compatible | LVPECL Compatible |  |
| 10 | DC Supply: | +15VDC @ 100 mA Max -15VDC @ 100 mA Max | +15VDC @ 87 mA -15VDC @ 36.1 mA |  |

| QA/QC Approval: |  | Date: |  |
| --- | --- | --- | --- |

INPUT VSWR