| Customer: | SNI Electronics, GA | Tested By: | E. Kretz |
| --- | --- | --- | --- |
| SO No: | SO16-207-PS-P (Line 02) | Temperature: | +25°C |
| Model No: | LM-6G18G-15-10W-SFF | Date: | 11/28/16 |
| Serial No: | PL20205/1647 | Drawing No: | 27612825 | Rev: | A1 |

| Test. Item No | PARAMETERS | SPECIFIED VALUE | TEST RESULTS | qa qc |
| --- | --- | --- | --- | --- |
| 1 | Frequency Range: | 6 GHz to 18 GHz | 6 GHz to 18 GHz See Plot |  |
| 2 | Insertion Loss @ 0 dBm Input: | 2.5 dB Typ. | 2.49 db See Plot |  |
| 3 | Peak Power | 10 Watts CW | Pass by Design |  |
| 4 | Leakage Power | +15 dBm Typ. | 12.5 dBm (See Typical Characteristics) |  |

| QA/QC Approval: |  | Date: |  |
| --- | --- | --- | --- |

Insertion Loss Plot