| Customer: | Shoshin Corp, Japan | Tested By: | K. Mansfield |
| --- | --- | --- | --- |
| SO No: | SO16-296-P-P | Temperature: | +25°C |
| Model No: | LM-1G2G4CW-1KWP-SMF | Date: | 01/05/17 |
| Serial No: | PL20368/1701 | Drawing No: | 27629433 | Rev: | A1 |

| Test. Item No | PARAMETERS | SPECIFIED VALUE | TEST RESULTS | qa qc |
| --- | --- | --- | --- | --- |
| 1 | Frequency Range | 1.0 GHz To 2.0 GHz | 1.0 GHz To 2.0 GHz See Plot |  |
| 2 | Insertion Loss | 0.7 dB Max | 0.69 dB See Plot |  |
| 3 | Input/Output VSWR | 2.0:1 Max @ -10 dBm Input | 1.6:1 See Plot |  |
| 4 | Impedance | 50 Ω | Pass |  |
| 5 | Input Power | 4 W CW Min 1 kW Peak (1% Duty Cycle, 1 µs Max Pulse Width) | Pass See Typical Characteristics |  |
| 6 | Maximum Flat Leakage | 16 dBm (40 mW) Max | 15.35dBm See Typical Characteristics |  |
| 7 | Limiting Threshold | 5 dBm Min, 1 dB Compression | 12.9 dBm |  |
| 8 | Recovery Time | 1 µs Max | 100ns See Typical Characteristics |  |
| 9 | Weight | 1 oz Typ. | 0.6 oz |  |
| 1. EXTERNAL DC BLOCKS ARE REQUIRED FOR PROPER FUNCTION. |

| QA/QC Approval: |  | Date: |  |
| --- | --- | --- | --- |

Insertion Loss and Return Loss