| Customer: | Shoshin Corporation, CA | Tested By: | L. McGraw |
| --- | --- | --- | --- |
| SO No: | SO17-441-P-E-002 | Temperature: | +25°C |
| Model No: | LM-400M2G-20-1W-SFF | Date: | 3/14/18 |
| Serial No: | PL22301/1811 | Drawing No: | 27634060 | Rev: | A1 |

| Test Item | PARAMETERS | SPECIFIED VALUE | TEST RESULTS | qa qc |
| --- | --- | --- | --- | --- |
| 1 | Frequency Range | 400 MHz to 2.0 GHz | 400 MHz to 2.0 GHz |  |
| 2 | Insertion Loss | 0.7 dB Max | 0.66dB (See Plot) |  |
| 3 | Leakage Power | 100 mW Max | 30.9mW |  |
| 4 | Spike Leakage | 0.1 erg. Max | 0.1 erg. Max |  |
| 5 | Recovery Time | 250 ns Max | <20ns (See Typical Characteristics) |  |
| 6 | VSWR | 2.0:1 Max | 1.57:1 (See Plot) |  |
| 7 | RF Power Handling | 1 W CW Max | Pass |  |
|  |  | 3 W Peak Max (1 µs PW, 0.1% DC) | Pass |  |

| QA/QC Approval: |  | Date: |  |
| --- | --- | --- | --- |

Insertion Loss and Return Loss