# SUMMARY TEST DATA

# ON

AMPLIFIER

NOTE: S21 is measured with a 20dB attenuator on the input.

| Test Item No. | PARAMETERS | SPECIFIED VALUE | MEASURED VALUE | REMARKS QA/QC |
| --- | --- | --- | --- | --- |
| 1 | Frequency Range: | 30MHz – 18GHz | Pass |  |
| 2 | Gain: | +38dB Typ. | Pass (See Plot) |  |
| 3 | Flatness: | (2.0dB Max. | (2.1dB | +0.1dB |
| 4 | *Noise Figure: | 5.0dB Max. | Pass (See NF Plot) |  |
| 5 | Pout @ 1dB Compression: | +12dBm Min. | > +12dBm |  |
| 6 | VSWR: | Input : 2.2:1 Output: 2.2:1 (Max.) | Pass (See plot) |  |
| 7 | DC Supply: | 300mA @ +12V Max. | 202mA @ +12V |  |

* This parameter is valid only above 500MHz

Production Manager Approval: ___ _______ Date: 08/15/06

QA/QC Approval: __________       ________ Date: 08/15/06

Swept S21 and S22 Plot

NOTE: S21 is measured with a 20dB attenuator on the input

Swept S11 Plot

Noise Figure Plot

(30MHz to 500MHz)

Noise Figure Plot

(500MHz to 18GHz)

# Text boxes

Tested By	: Kevin Mason

## Temperature	: +25(C

Date		: 08/15/06

Customer	: EM Electronics Corp.

Job No	: PE606048

Model No	: PEC-38-30M18G-12-SFF

Serial No	: PL2647

5715 Industry Lane, Unit 11, Frederick, MD 21704 USA  Phone: (301)662-5019  Fax: (301)662-1731

email: sales@planarelec.com

5715 Industry Lane, Unit 11, Frederick, MD 21704 USA  Phone: (301)662-5019  Fax: (301)662-1731

email: sales@planarelec.com

5715 Industry Lane, Unit 11, Frederick, MD 21704 USA  Phone: (301)662-5019  Fax: (301)662-1731

email: sales@planarelec.com

5715 Industry Lane, Unit 11, Frederick, MD 21704 USA  Phone: (301)662-5019  Fax: (301)662-1731

email: sales@planarelec.com

5715 Industry Lane, Unit 11, Frederick, MD 21704 USA  Phone: (301)662-5019  Fax: (301)662-1731

email: sales@planarelec.com