# SUMMARY TEST DATA

| Test Item No. | PARAMETERS | SPECIFIED VALUE | MEASURED VALUE | REMARKS QA/QC |
| --- | --- | --- | --- | --- |
| 1 | Frequency Range: | 25 MHz to 80 MHz | 25 MHz to 80 MHz |  |
| 2 | Insertion Loss @ 0dBm Input: | -1.5dB Max. | -0.04dB |  |
| 3 | Input & Output VSWR @ 0dBm: | 2.0 : 1 Max. | 1.02:1 |  |
| 4 | Input Power Level: | CW In-Band: 10 W CW Out of Band: 20 W | Pass by design |  |
| 5 | Output Limiting: | +15 dBm Max. | +10.45 dBm |  |
| 6 | Recovery Time: | 1usec Max. | Pass by design |  |

Production Manager Approval:                                                           Date: ___________

QA/QC Approval:                                                                                  Date: ___________

# Text boxes

Tested By	: Hugo Gonzales

## Temperature	: +25(C

Date		: 01/29/11

Customer	: Rockwell Collins Govt Systems

Job No	: SO10-215-P

Model No	: LM-20M80M-10-20W

Serial No	: PL8595