# SUMMARY TEST DATA ON SDLVA

| TEST ITEM NO: | PARAMETERS | SPECIFIED VALUE | MEASURED VALUE | REMARKS QA/QC |
| --- | --- | --- | --- | --- |
| 1 | FREQUENCY RANGE | 0.1 TO 2.0 GHz | 0.1 TO 2.0 GHz |  |
| 2 | DYNAMIC RANGE | 70 dB MINIMUM, 75 dB TYPICAL | SEE PLOTS |  |
| 3 | LOG LINEARITY @ -65 TO +5 dBm -50 TO +5 dBm @ 100 MHz | ± 2.0 dB MAXIMUM | 1.80 dB |  |
| 4 | LOGGING RANGE | -65 dBm MINIMUM +5 dBm MAXIMUM | SEE PLOTS |  |
| 5 | INPUT VSWR | 2.0:1 MAXIMUM 1.8:1 TYPICAL | SEE TYPICAL CHARACTERISTICS |  |
| 6 | TSS | -65 dBm (-70 dBm TYPICAL) | SEE TYPICAL CHARACTERISTICS |  |
| 7 | LIMITED IF OUTPUT | +10 dBm TYPICAL | 7.76dBm 11.93dBm |  |
| 8 | MAXIMUM RF INPUT POWER | +10 dBm | PASS BY DESIGN |  |
| 9 | LOG VIDEO OUTPUT COUPLING | DC | PASS BY DESIGN |  |
| 10 | MAXIMUM OUTPUT VOLTAGE | 2.7 V MAXIMUM | SEE PLOTS |  |
| 11 | RISE TIME | 25 nSec MAXIMUM | SEE TYPICAL CHARACTERISTICS |  |
| 12 | FALL TIME | 30 nSec MAXIMUM | SEE TYPICAL CHARACTERISTICS |  |
| 13 | SETTLING TIME | 40 nSec MAXIMUM | SEE TYPICAL CHARACTERISTICS |  |
| 14 | DC OFFSET | 0.1 V NOMINAL (ADJUSTABLE) | PASS |  |
| 15 | LOG VIDEO SLOPE | 25 mV/dB NOMINAL @ 1 GHz | 11.9mV/dB |  |

| 16 | LOG VIDEO SLOPE VARIATION WITH FREQUENCY | ± 0.5mV/dB TYPICAL (OVER 80 MHz RF BANDWIDTH) | SEE PLOTS |  |
| --- | --- | --- | --- | --- |
| 17 | LOG VIDEO SLOPE VARIATION WITH TEMPERATURE | ± 0.5mV/dB TYPICAL | SEE TYPICAL CHARACTERISTICS |  |
| 18 | PROPAGATION DELAY | 10 nS TYPICAL | SEE TYPICAL CHARACTERISTICS |  |
| 19 | VIDEO LOAD | 100 Ω ± 10% | 100 Ω |  |
| 20 | DC POWER +V (NO LOAD) | 7 to 18V @ 300 mA MAXIMUM | 115mA |  |
| 21 | DC POWER –V (NO LOAD) | -7 to -18V @ 150 mA MAXIMUM | 141mA |  |

| TESTED ON: |  |  |  |
| --- | --- | --- | --- |
| QA / QC APPROVAL: |  | DATED: |  |

# Text boxes

Tested By	: Hugo Gonzales

## Temperature	: +25(C

Date		: 02/24/11

Customer	: Rubisoft

Job No	: SO11-017-P

Model No	: SDLVA-0120-70 OPT 100M2G, 10DBM

Serial No	: PL8688